## Slide 1
An FPGA toolchain for
Graph Neural Network
acceleration using
High-Level Synthesis
AUTHOR
DEMASI GIOVANNI
ADVISOR
FABRIZIO FERRANDI
CO-ADVISORS
SERENA CURZEL, MICHELE FIORITO

## Slide 2
02
Contents
01
Introduction
- motivations
- objectives
- background
- state of the art
02
Solution
- Proposed toolchain
- experiments
- matrix multiplication
acceleration
- GCN accelerator
- model accuracy
03
Conclusion
- solution analysis
and comparison
- future developments

## Slide 3
03
Thesis motivations and objectives
Growing popularity of Graph Neural Networks in past years
Mostly used in domains characterized by vast amounts of data, such as social networks and chemistry
Main goal of this thesis was to develop a comprehensive toolchain for Graph
Neural Network inference acceleration
on FPGA architectures

## Slide 4
04
Graph Neural Networks
Deep learning techniques that operate on graph-structured data to solve prediction tasks
Graph Neural Networks consist of multiple interconnected layers and typically encompasses three main stages
pre-processing
Iterative updates
readout

## Slide 5
05
MLIR and High-Level Synthesis
C/C++
HLS tool
VHDL/Verilog
input design
output RTL
- A novel approach to construct
reusable and extensible compiler
infrastructure
- Reduces the effort to build
domain-specific compilers.
- Simplified hardware development
- Reduces design time and effort
- Final implementation’s functionality
independent of hardware design
knowledge
MLIR
High-Level Synthesis

## Slide 6
06
State of the art GNN accelerators
Unified
architecture
AWB-GCN
ENG
Tiled
architecture
Auten et al.
Hybrid
architecture
HyGCN
GRIP
SW-HW
Co-design
Zhang et al.
GCoD
High-Level Synthesis based
FlowGNN is a GNN acceleration framework utilizing
High-Level Synthesis.
C++ model implementations ready to be synthesized.
C++ models
FlowGNN
Accelerator

## Slide 7
07
Design of the toolchain
PyTorch
Popular framework for neural network implementations.
Torch-MLIR
enables the generation of the MLIR representation.
Synthesizer
The MLIR representation serves as input for the synthesizer. Frontend optimization are applied, then the refined version proceeds to the backend, where the actual GNN accelerator is effectively produced.

## Slide 8
08
Toolchain inputs
GCN model
Cora dataset
- Implemented in PyTorch
- Two convolutional layers
- Convolutional layers made
of two matrix multiplications
- Task is node classification
- scientific publications
- multiclass classification
Name | Nodes | Words | Links | Classes
Cora | 2708 | 1433 | 5429 | 7
Cora15 | 15 | 15 | 3 | 7
Cora30 | 30 | 30 | 4 | 7
Cora60 | 60 | 60 | 8 | 7
Cora90 | 90 | 90 | 18 | 7
Cora120 | 120 | 120 | 22 | 7
Cora150 | 150 | 150 | 37 | 7
Datasets used for experiments; subsets of Cora dataset

## Slide 9
09
Performance analysis
Name | %
aten::mm | 50.25%
aten::addmm | 36.30%
aten::add | 4.64%
aten::mm=matrix multiplication; aten::add=
matrix sum; aten::addmm=matrix
multiplication plus, matrix sum
Model analysis
>50% of the computational
time used by matrix
multiplication
PyTorch matrix multiplication analysis
sparse matrix multiplication faster than dense
for big matrix sizes with sparsity 0.001

## Slide 10
10
From PyTorch to MLIR
Torch script is an intermediate representation used to generate serializable and optimizable models directly from PyTorch code; it represents the bridge between PyTorch and Torch-MLIR.
The model must be adapted to Torch Script, then it can be compiled using Torch-MLIR to obtain its MLIR representation.
Model PyTorch
implementation
Adapt model
to Torch Script
torch_mlir.compile
MLIR representation
Training

## Slide 11
11
Synthesis
- high level optimization
- subset of MLIR optimization
passes
- output represent the input of
Panda-Bambu
SODA-OPT
PandA-Bambu
MLIR representation
Outline kernel function
High level optimizations
Low-Level IR
Low-Level IR
Low level optimizations
RTL IR
Accelerator
- HLS tool
- last phase of synthesis
- low level optimizations
- output the final accelerator

## Slide 12
12
FPGA-accelerated matrix multiplication
Understanding how to optimize matrix
multiplication, the model bottleneck.
Comparative analysis between PyTorch matrix multiplication operation and the baseline accelerator performance.
The baseline accelerator is faster than PyTorch when matrices are relatively small. The reasons behind this behaviour may lie in the fact that:
- the generated accelerator assumes that all data is available in BRAM
- PyTorch times have been measured using all the eight available threads on
the machine, exploiting more parallelism with respect to the accelerator.

## Slide 13
13
Synthesis optimizations
Loop unrolling
Parallel memory access
for i in range(0,4){
code
}
- increasing the number of memory
channels
- better exploitation of available
parallelism
- more parallel memory accesses
but more cycles due to external
memory
for i in range(0,2){
code
code
}
before
after
- expanding completely or partially
the loop
- unroll factor parameter to decide
the number of loop iterations to
unroll
- more chances of parallelization
1 | 3 | 0
2 | 8 | 3
3 | 2 | 6
data
read

## Slide 14
14
Optimized matrix multiplication accelerator
- Low available parallelization = using two
channels and storing all memory
objects in BRAMs is the best option
- High available parallelization = 32
channels with external memory
- 2 channels with external memory is the
least favourable choice - External memory beneficial when large
volume of data can be simultaneously
loaded and stored to offset the additional
cycles required for external
memory access
Cycles comparison between configurations with different number of channels with BRAM/external memory.

## Slide 15
15
GCN accelerator
- analysed synthesis optimizations
applied to the GCN model
- optimized accelerator uses two
channels with on-chip BRAMs
and one full unroll of the
innermost loop
- it outperforms PyTorch
- advantage maintained also with
bigger dataset sizes
Graph Convolutional Network inference time comparison between PyTorch and FPGA implementations for different sizes of the dataset.

## Slide 16
16
GCN accelerators comparison
analysis to show how the accelerator has been affected by the loop unrolling technique with respect to the baseline performance
- optimized accelerator uses
two channels and one full
unrolling of the innermost
loop
- the speedup increases as
the size of the dataset
increases
- trade-off between
performance and area
Graph Convolutional Network number of cycles comparison between baseline and optimized accelerators for different sizes of the dataset.

## Slide 17
17
Model accuracy
Dataset | PyTorch | Accelerator |  | 
Cora15 | 0.333 | 0.333 | 1.31E-06 | 0.26E-06
Cora30 | 0.333 | 0.333 | 8.64E-06 | 0.54E-06
Cora60 | 0.166 | 0.166 | 4.02E-06 | 0.25E-06
Cora90 | 0.555 | 0.555 | 19.47E-06 | 0.45E-06
Cora120 | 0.291 | 0.291 | 19.86E-06 | 0.27E-06
Cora150 | 0.533 | 0.533 | 23.84E-06 | 0.30E-06
Dataset | PyTorch | Accelerator |  | 
Cora15 | 0.333 | 0.333 | 1.31E-06 | 0.26E-06
Cora30 | 0.333 | 0.333 | 8.64E-06 | 0.54E-06
Cora60 | 0.166 | 0.166 | 4.02E-06 | 0.25E-06
Cora90 | 0.555 | 0.555 | 19.47E-06 | 0.45E-06
Cora120 | 0.291 | 0.291 | 19.86E-06 | 0.27E-06
Cora150 | 0.533 | 0.533 | 23.84E-06 | 0.30E-06
- understandably low accuracy
- synthesis has not impacted the
accuracy of the model
- the average error is stable even
for increasing graph sizes
- very low probability of
misclassification even when
dealing with large dataset
Accuracy comparison between PyTorch and Accelerator. 𝝐=total error; =average error.

## Slide 18
18
Proposed solution analysis
Characteristic | State of the art | FlowGNN | Toolchain
Supported models | mostly focused on a specific model, only some solution are generalizable | Set of implementations in C++ that can be modified | All models that can be implemented in PyTorch
Customization | mostly not customizable, only few propose some settable parameters | Four configurable parallelization parameters | Optimization during synthesis, fine-tuning of model performance
Hardware design | mostly required, only one solution uses HLS tools | Use of HLS, no need of low-level programming | Use of HLS, no need of low-level programming
FlowGNN is the only state of the art solution using HLS
New model and features should be implemented in C++ a possible blocking factor
Limited possibility
of customization to
specific needs
About FlowGNN

## Slide 19
19
Conclusions and future developments
Accomplishments
- Toolchain for GNN inference acceleration
- Matrix multiplication and GCN accelerators
with fine-tuned optimizations
- Analysis of SODA and Bambu optimizations
- Implementation of new Torch-MLIR feature
- Identification of possible area of
improvements of Torch-MLIR
Future developments
- Support of PyTorch Geometric
- Support of sparse tensor operations,
possible solution is PyTaco

## Slide 20
Thanks for your
attention
GIOVANNI DEMASI, 2023