## Slide 1
An FPGA toolchain for
Graph Neural Network
acceleration using
High-Level Synthesis
AUTHOR
GIOVANNI DEMASI
ADVISOR
FABRIZIO FERRANDI
CO-ADVISORS
SERENA CURZEL, MICHELE FIORITO

## Slide 2
02
Contents
01
Introduction
background
motivations
objectives
02
Solution
toolchain
contributions
experiments
03
Conclusion
solution analysis and comparison
future developments

## Slide 3
03
Graph Neural Networks
Graph Neural Networks are deep learning techniques that operate on graph-structured data to solve prediction tasks:
Graph Neural Networks consist of multiple interconnected layers, and they typically encompass three main stages:
pre-processing
Iterative updates
readout
transforming
the input data
edge and vertex feature vectors update
aggregates embeddings
in a global feature vector
Classify nodes according to
labels of their neighbours
Classify the whole graph into
different categories
Predict the evolution of connection between two entities
Growing popularity of Graph Neural Networks in past years on Google Scholar.

## Slide 4
04
Thesis motivations and objectives
Objectives of the thesis
A comprehensive toolchain for Graph Neural Network inference acceleration on FPGA architectures
  Analysis of state-of-the-art tools for Graph Neural Network implementation;
  Identify the GNN models bottlenecks and accelerate the heaviest computational tasks
  Design space exploration of optimizations designed to finely enhance model performance
Motivations of the thesis
Optimize and accelerate the capabilities of Graph Neural Networks is necessary due to their increasingly popularity, especially in fields characterized by vast amount of data.
Example of graph-structured data on which Graph Neural Networks can operate

## Slide 5
05
Proposed toolchain
Synthesizer
It takes the MLIR representation as input and transform it into accelerator. Firstly, it applies high-level optimizations, then the refined version proceeds to the Bambu HLS backend, where the GNN accelerator is effectively produced.
A novel approach to construct reusable
and extensible compiler infrastructure.
MLIR
The toolchain proposed in this thesis makes use
of MLIR and is based on High-Level Synthesis.
C/C++
HLS tool
VHDL
High-Level Synthesis
Simplified hardware development.
Reduces design time and effort.
FPGA Toolchain for Graph Neural Network Acceleration. Main thesis contributions represented in green.

## Slide 6
06
Contributions
The main contributions of this thesis are:
Analysis of the existing tools for the implementation of Graph Neural Networks;
Identification of missing features of Torch-MLIR and implementation of some of them;
Analysis of bottlenecks in the execution of a Graph Convolutional Network;
Exploration of the combination of SODA-OPT and PandA-Bambu optimizations, leading to the development of a novel default optimization pipeline for Graph Neural Networks.
The proposed GNN optimization pipeline allows to achieve an average of more than 3x improvement in inference time on FPGA.
FPGA Toolchain for Graph Neural Network Acceleration. Main thesis contributions represented in green.

## Slide 7
07
Toolchain inputs
Graph Convolutional Network
Cora dataset
Model’s characteristics:
Two convolutional layers
Convolutional layers made of two matrix multiplications
Task is node classification
Scientific publications
Multiclass classification
Subsets to contain synthesis and evaluation times
Name | Nodes | Words | Links | Classes
Cora | 2708 | 1433 | 5429 | 7
Cora15 | 15 | 15 | 3 | 7
Cora30 | 30 | 30 | 4 | 7
Cora60 | 60 | 60 | 8 | 7
Cora90 | 90 | 90 | 18 | 7
Cora120 | 120 | 120 | 22 | 7
Cora150 | 150 | 150 | 37 | 7
Datasets used for experiments: subsets of Cora dataset.
PyTorch
Proposed toolchain entry point, for neural network implementations.

## Slide 8
08
From PyTorch to MLIR
PyTorch model
implementation
Adapt model
to Torch Script
torch_mlir.compile
MLIR IR
Model training
From PyTorch model implementation to MLIR IR flow
Torch-MLIR
The Torch-MLIR project aims to provide first class compiler support from the PyTorch ecosystem to the MLIR ecosystem.
It leverages Torch script, an intermediate representation used to generate serializable and optimizable models directly from PyTorch code; it represents the bridge between PyTorch and Torch-MLIR.
After having created a set of general rules to adapt different GNN models to Torch script, they have been applied to the GCN model obtaining its Torch script compatible version; then it has been compiled using Torch-MLIR to obtain its MLIR representation.

## Slide 9
09
Synthesis
High level optimization
Subset of MLIR passes
Output represents the input of Panda-Bambu
SODA-OPT
PandA-Bambu
MLIR representation
Outline kernel function
High level optimizations
Low-Level IR
Low-Level IR
Low level optimizations
RTL IR
Accelerator
High-Level Synthesis tool
Low level optimizations
Output is the final accelerator
The synthesizer, which includes SODA-OPT and PandA-Bambu and represents the final step of the toolchain, optimizes and synthesizes the MLIR representation, targeting FPGA.

## Slide 10
10
GNN profiling on CPU
Name | %
aten::mm | 50.25%
aten::addmm | 36.30%
aten::add | 4.64%
aten::mm=matrix multiplication; aten::add=
matrix sum; aten::addmm=matrix
multiplication plus matrix sum
Model analysis
>50% of the computational
time used by matrix
multiplication
PyTorch matrix multiplication analysis
sparse matrix multiplication faster than dense
for big matrix sizes with density 0.001
Analysis to identify the computational
bottlenecks of the model
PyTorch CPU execution time of matrix multiplication with
dense and sparse matrix representations. COO=Coordinate list; CSR=Compressed Sparse Row

## Slide 11
11
FPGA-accelerated matrix multiplication
Analysis results
Baseline accelerator faster than PyTorch for small matrices. Possible reasons:
Accelerator assumes all data in BRAM
PyTorch exploits more parallelism by using all available threads
CPU
Intel Core i9, 8
cores, 2.3 GHz
Accelerators
AMD Virtex UltraScale+ (Alveo U280) FPGA.
Experimental phase setup
Baseline
PyTorch CPU execution, 8 threads
Outcome
FPGA matrix multiplication accelerator, from ~17x to ~0.6x times faster, according to the size of the dataset
Experiment
Matrix multiplication synthesis through the proposed toolchain, without optimizations

## Slide 12
12
Synthesis optimizations
Loop unrolling
Parallel memory access
for i in range(0,4){
code
}
Increasing number of mem channels for more parallel mem accesses
Better exploitation of parallelism
More parallel memory accesses but more cycles due to external memory
for i in range(0,2){
code
code
}
before
after
Expanding completely or partially the loop, according to unroll factor
Unroll factor parameter to decide the number of loop iterations to unroll
More chances of parallelization
1 | 3 | 0
2 | 8 | 3
3 | 2 | 6
data
read
To make the accelerator able to exploits more parallelism, two main optimizations have been applied: loop unrolling and parallel memory accesses.

## Slide 13
13
Optimized matrix multiplication accelerator
Analysis results
External memory beneficial for large unroll factor: parallel load of many data offsets the additional cycles required for external memory
Baseline
FPGA matrix multiplication accelerator with BRAM and 2 memory channels
Outcome
FPGA matmul accelerators exploiting increased unroll factors and external memory, with 2, 16 and 32 memory channels
Experiment
Matrix multiplication synthesis through the proposed toolchain, with BRAM and external memory, to analyse execution cycles with different number of channels and unroll factors

## Slide 14
GCN accelerator
Analysis results
Accelerator outperforms PyTorch
Performance improvement maintained with increasing dataset sizes
Synthesis has not impacted the accuracy of the model
Baseline
PyTorch CPU execution, 8 threads
Outcome
FPGA baseline and optimized accelerators; optimized accelerator uses 2 memory channels with BRAMs and one full unroll, and it achieves an average of more than 3x improvement in inference time.
Experiment
Automated synthesis of the GCN model with the new optimization pipeline from Design Space Exploration.
14

## Slide 15
15
State of the art analysis
Characteristic | State of the art | FlowGNN | Proposed toolchain
Supported models | Mostly focused on a specific model, only some solutions are generalizable | Set of implementations in C++ that can be modified | Any models that can be implemented in PyTorch
Customization | Mostly not customizable, only few propose some settable parameters | Four configurable parallelization parameters | Optimization during synthesis, fine-tuning of model performance
Hardware design | Mostly required, only one solution uses HLS tools | Use of HLS, no need of low-level programming | Use of HLS, no need of low-level programming
The proposed toolchain offers new and improved ways to accelerate Graph Neural Network inference time on FPGA architectures.

## Slide 16
16
Conclusions and future developments
Accomplishments
FPGA toolchain for GNN inference acceleration
Enhanced compatibility of toolchain elements
  General set of rules to make models compatible with torch script
  Support of constant of tuple Type in Torch-MLIR
  Identification of area of improvements for PyTorch Geometric support
Matrix multiplication and GNN accelerators with customized optimizations to finely enhance their performance
Future developments
Support of PyTorch Geometric
Support of sparse tensor operations, possible solution is PyTaco
Possible future developments to the proposed toolchain in red

## Slide 17
Thanks for your
attention
GIOVANNI DEMASI, 2023

## Slide 18
06
State of the art GNN accelerators
Unified
architecture
AWB-GCN
ENG
Tiled
architecture
Auten et al.
Hybrid
architecture
HyGCN
GRIP
SW-HW
Co-design
Zhang et al.
GCoD
High-Level Synthesis based
FlowGNN is a GNN acceleration framework utilizing
High-Level Synthesis.
C++ model implementations ready to be synthesized.
C++ models
FlowGNN
Accelerator

## Slide 19
05
MLIR and High-Level Synthesis
C/C++
HLS tool
VHDL/Verilog
input design
output RTL
- A novel approach to construct
reusable and extensible compiler
infrastructure
- Reduces the effort to build
domain-specific compilers.
- Simplified hardware development
- Reduces design time and effort
- Final implementation’s functionality
independent of hardware design
knowledge
MLIR
High-Level Synthesis

## Slide 20
15
GCN accelerators comparison
Analysis to show how the accelerator using 2 channels with BRAMs and one full unroll
of the innermost loop has been affected by loop unrolling technique, compared to the baseline performance with 2 channels BRAMs and unroll factor equal to 1.
The baseline accelerator does not exploit parallelism at all
The optimized accelerator exploits parallelism more and more as the size of the dataset increases; consequently, the speedup increases as the size of the dataset increases
Trade-off between performance and area: more parallel operations means more computational units
Graph Convolutional Network number of cycles comparison between baseline and optimized accelerators for different sizes of the dataset.

## Slide 21
17
Model accuracy
Dataset | PyTorch | Accelerator |  | 
Cora15 | 0.333 | 0.333 | 1.31E-06 | 0.26E-06
Cora30 | 0.333 | 0.333 | 8.64E-06 | 0.54E-06
Cora60 | 0.166 | 0.166 | 4.02E-06 | 0.25E-06
Cora90 | 0.555 | 0.555 | 19.47E-06 | 0.45E-06
Cora120 | 0.291 | 0.291 | 19.86E-06 | 0.27E-06
Cora150 | 0.533 | 0.533 | 23.84E-06 | 0.30E-06
Dataset | PyTorch | Accelerator |  | 
Cora15 | 0.333 | 0.333 | 1.31E-06 | 0.26E-06
Cora30 | 0.333 | 0.333 | 8.64E-06 | 0.54E-06
Cora60 | 0.166 | 0.166 | 4.02E-06 | 0.25E-06
Cora90 | 0.555 | 0.555 | 19.47E-06 | 0.45E-06
Cora120 | 0.291 | 0.291 | 19.86E-06 | 0.27E-06
Cora150 | 0.533 | 0.533 | 23.84E-06 | 0.30E-06
Accuracy comparison between PyTorch and Accelerator. 𝝐=total error; =average error.
Synthesis has not impacted the accuracy of the model
Average error is stable; not affected by the dataset size
Low probability of misclassification even when dealing with large dataset
Analysis to measure difference in floating precision on FPGA implementations and its impact on model accuracy.

## Slide 22
17
GCN accelerator: area and power
Dataset | Optimizations | Cycles | Slices | Luts | Registers | DSPs | BRAMs | Frequency (MHz) | Power (mW)
Cora15 | 1 Full unroll 32 channels | 93,705 | 8,338 | 35,265 | 35,164 | 44 | 256 | 179.08 | 4.25
Cora30 | 1 Full unroll 32 channels | 301,800 | 12,448 | 50,907 | 50,558 | 74 | 256 | 168.12 | 4.47
Cora60 | 1 Full unroll 32 channels | 1,064,580 | 21,726 | 94,025 | 77,956 | 134 | 256 | 149.20 | 5.07
Cora90 | 1 Full unroll 32 channels | 2,298,510 | 32,046 | 154,917 | 108,770 | 194 | 256 | 154.20 | 5.44
Cora120 | 1 Full unroll 32 channels | 3,987,840 | 43,187 | 218,178 | 135,961 | 254 | 256 | 134.49 | 6.06
Cora150 | 1 Full unroll 32 channels | 6,136,470 | 27,002 | 115,463 | 143,916 | 26 | 264 | 149.20 | 6.33